## Slide 1: Design of Engineering Experiments
Chapter 7
7.1-7.3 only

## Slide 2: Experiment
Need volunteers who
  are male or female
  who have or have not had a(n) energy/caffeine drink in the last hour
Take your resting pulse (beats per minute)
Turn in paper with above info as follows:
Gender: M or F
Energy/Caffeine Drink: Y or N
Resting Pulse: bpm value
H0 : Gender does not affect resting pulse
H1 : Gender affects resting pulse
H0 : Drinking an energy/caffeine drink does not affect resting pulse
H1 : Drinking an energy/caffeine drink affects resting pulse
H0 : Gender and drinking an energy/caffeine drink interactively do not affect resting pulse
H1 : Gender and drinking an energy/caffeine drink interactively affect resting pulse

## Slide 3: The 2k Factorial Design
A 2k factorial design is one that has two factors (usually denoted A and B), each run at k levels.
The simplest 2k design is a 22 design.
  Factor A is run at two levels: “low” and “high”
  Factor B is run at two levels: “low” and “high”
    Low and High are relative…could be “Operator 1 and Operator 2”, or “Condition 1 and Condition 2”
Each combination of factor levels is called a treatment

## Slide 4
A: the (estimated) main effect of Factor A.
It is a numerical value showing the average change as we move from the low level of Factor A to the high level of Factor A.
B: the (estimated) main effect of Factor B.
It is a numerical value showing the average change as we move from the low level of Factor B to the high level of Factor B.
AB: the (estimated) interactive effect of Factors A and B together.
It is a numerical value showing the average change as we move from the low level of Factor A/high level of Factor B to the high level of Factor A/low level of Factor B.
+ and - denote the factor setting for a run.
  + = high
  - = low

## Slide 5: Computing Effects
Factor | Blow | Bhigh
Alow | 10 | 20
Ahigh | 30 | 40
Table 1. Factorial Experiment Without Interaction
Note: there is only a sample of one per treatment here

## Slide 6
Factor | Blow | Bhigh
Alow | 10 | 20
Ahigh | 30 | 0
Table 2. Factorial Experiment With Interaction

## Slide 7
Part I. We will do three hypothesis tests using ANOVA:
Part II. We will develop a regression model to predict response:

## Slide 8: Excel Tutorial: 22 Factorial Design Analysis
Part I: Hypothesis Tests using ANOVA

## Slide 9
Factor A: Material Type Factor B: Temperature
Y: battery life (hours)
Low
Factor A
High
Factor B
Low High
Example

## Slide 10: 1. Input data such that Factor A is the rows and Factor B is the columns

## Slide 11: 2. Go to Data then Data Analysis then ANOVA Two Factor with Replication

## Slide 12: 3. Fill in dialogue window. Include labels. Click OK.

## Slide 13
4. Interpret output
Sample: Factor A (Material)
Column: Factor B (Temperature)
Sample corresponds to Material. P-value is .252. Fail to reject H0.
Columns corresponds to Temperature. P-value is .001. Reject H0.
Interaction corresponds to interaction of Material and Temperature. P-value is .556.
Fail to reject H0.

## Slide 14: Tutorial: How to compute numeric values of relevant constants
Part II: Regression Model

## Slide 15: Regression Model
Y is the modeled response
x1 is the value of Factor A (+1 or -1)
x2 is the value of Factor B (+1 or -1)
x1x2 is the interactive value of Factors A and B (+1 or -1)
are numerical coefficients (constants)
n is the number of replicates

## Slide 16: Algorithm
1. From Part I, determine which of the bi are significant (you will always compute b0 , however).
2. Compute the estimate of b0, ybar, the Main Effect of Factor A (A), the Main Effect of Factor B (B) and the Interactive Effect (AB) as needed
  Recall that A is the difference between the average response when A is high and the average response when A is low
  Recall that B is the difference between the average response when B is high and the average response when B is low
  Recall that AB is the difference between the diagonal average responses
Problem 7-1 data
Low
Factor A
High
Factor B
Low High
Important note: For this problem, you would NOT have to compute A or AB, because the we failed to reject H0 for those effects. The computations are shown here, however, in the event that you DO need to compute them for another data set.

## Slide 17
3. Develop the (final) linear model for the response
For Problem 7-1, we need only compute b0 and b2 because they are the only significant contributors to the response, battery life

## Slide 18: Questions You Should Know Answers To For The Final Exam
An engineer suspects that the surface finish of metal parts is influenced by the type of paint used and the drying time. She selects two drying times: 20 minutes and 30 minutes. She selects two types of paint. Three parts are tested with each combination of paint type and drying time. The data and ANOVA Excel output are shown below:
ANOVA |  |  |  |  |  | 
Source of Variation | SS | df | MS | F | P-value | F crit
Sample | 0.083333333 | 1 | 0.083333 | 0.000444 | 0.983704 | 5.317655
Columns | 24.08333333 | 1 | 24.08333 | 0.12833 | 0.729438 | 5.317655
Interaction | 1140.75 | 1 | 1140.75 | 6.078597 | 0.038984 | 5.317655
Within | 1501.333333 | 8 | 187.6667 |  |  | 
Total | 2666.25 | 11 |  |  |  | 
 | Drying Time (min) | 
Paint | 20 | 30
1 | 74 | 78
 | 64 | 85
 | 50 | 92
2 | 92 | 66
 | 86 | 45
 | 68 | 85
What are the null hypotheses being tested?
Is the Paint factor significant? If so, what is the Main Effect of Paint?
Is the Drying Time factor significant? If so, what is the Main Effect of Drying Time?
Is the Interaction of Paint and Drying Time significant? If so, what is the Main Effect of this interaction?
What is the regression model that results from the Excel output and your computations of the constants in the model?
If we use Paint 2 and a 20-minute drying time, what is the predicted value for the surface finish using the model?
Use a = .05
Significant means you should include that term in the final model.